## Slide 1
Live Shipment Tracker
Team Optimus
Arnab Paul Choudhury, Mtech IIT Guwahati
Aryan Yadav, Mtech IIT Guwahati
Manas Ranjan Jena, PhD NIT Rourkela

## Slide 2
Challenge:
Develop a low-cost light weight tracker with real-time information on High value Items
E-commerce Marketplace
Seller
Customer
Third-party Logistic Support
location?
Key Players and Current scenario:
High Value Package
#1

## Slide 3
Problems Faced:
Total dependence on logistic partner for tracking package location
No real-time visibility
Items are sometimes lost in Transit
Some items are marked as “Return to Origin” without attempting delivery
Seller has no idea whom to trust in the case of a dispute
#2

## Slide 4
Solution:
The major components of the solution:
Tracking hardware device
  Collect location information from satellites/network
  Transmit location information
Private and Permissioned Blockchain Network
  Ensures immutability of data
  Enhanced security
Application Server
  Receive data
  Visualize data
  Process data
#3

## Slide 5
Architecture Diagram:
Microcontroller
Persistence Storage
GPS/GNSS Module
GPRS/LTEModule
Application Server
Blockchain network
Client Device Application
Satellite
Internet
Tracker Device
Cloud
Wireless connection
Wired connection
Connection
Legend
Server
#4

## Slide 6
Tracker Device:
Form factor: 5.3x4.7x3 cm
Lifetime: 1 month
Power source: 2000 mAh batteries
Frequency of Transmission: 1 per 15 minutes
Major Components Used:
SIM7000JC: GPRS/LTE/GPS
ESP-12e: Microcontroller with SPIFFS
SD card (optional, for more persistent storage)
Dual use Antenna for GPS and LTE
Major constraints to form factor and lifetime:
Frequency of transmission
Energy density of Battery
Type of Technology used for Transmission
5.3 cm
3 cm
4.7 cm
Fig: PCB with SD card
(bottom view)
Fig: PCB without SD card (Bottom view)
Fig: PCB top view
Fig: Dimensions of tracking device
#5

## Slide 7
Flowchart:
#6

## Slide 8
Blockchain Network:
Type of Blockchain network:
Permissioned Private Blockchain
Benefits:
Immutability
Security
Faster transactions; better performance
Seller
Logistic Partner 1
Logistic Partner 2
Customer 1
Customer 2
Customer 3
Validating peer
#7

## Slide 9
Prototype Demonstration:
Components and technologies used:
Tracker:
SIM900A, development board
Internet connectivity(GPRS connection): SIM
Microcontroller: NodeMCU, ESP-12e development board
GPS module: Neo-6m
Server:
Http tunnel for localhost: ngrok
Python flask
Blockchain:
Python
Application Server:
Python Flask
HTML/Css
Javascript
Mapbox
SIM900A development board
NodeMCU
Neo-6m GPS Module
SIM
Tracker
Internet
ngrok
Blockchain
Application Server
Local Machine
Data Server
#10

## Slide 10
Estimated Costs:
Serial No. | Component | Unit cost | Units required | Cost
1 | SIM7000JC | 1500 | 1 | 1200
2 | ESP-12e | 200 | 1 | 200
3 | Battery(2000 mAh) |  |  | 400
4 | Dual Antenna |  |  | 200
5 | Passive elements |  | As per requirement | 100
6 | Active elements |  | As per requirement | 100
7 | Fabrication |  |  | 300
8 | Transistors, USB, regulators and other components |  |  | 300
9 | Tracker frame |  |  | 200
 |  |  | Total | 3000
Per unit Tracker Cost:
Data Charges: Depends upon service provider, however it is minimal
Server, Blockchain: multiple low cost and “pay as you go” cloud options available with initial cost almost nil and charges are correlated with the amount of active usage, like API calls etc.
To sum up, the entire solution can be deployed within Rs 4000
#9

## Slide 11
Benefits and Advantages:
No human intervention required once embedded in package
Cost effective, small form factor
Blockchain ensures immutability and security
Data is Decentralized, yet private and permissioned
Customer satisfaction
#10

## Slide 12
Future Work:
Make use of technologies like Nb-IoT/LoRa/5G
Optimized use of microcontroller
Implement industry grade Blockchain framework like Hyperledger framework etc.
Unique visualization for providing information at a glance.
#11

## Slide 13
Questions…